## Slide 1: DRAG REDUCTION SYSTEM PROJECT
Master degree in Mechatronics Engineering Mechatronic Systems Simulation
Albi Matteo Consalvi Natale Pettene Mattia
Academic Year 2021 - 2022

## Slide 2: SYSTEM DESIGN REQUIREMENTS
High aerodynamic efficiency
High precision
Quick motion
Low power consumption
Compliance with rules
Easy to assemble
Durability
Structurally safe
Lightweight

## Slide 3
SYSTEM DESIGN MATCHING REQUIRIMENTS AND SPECIFICATION

## Slide 4
SYSTEM DESIGN EXISTING SOLUTION COMPARISON
PUSH-UP
Simple and economic
Easy access to hydraulics
Great actuator’s effort
Disturbances
POD-ROCKER
Low actuator’s effort
Eliminate disturbances
Higher costs
Complexity
POD-PULL
Simple and economic
Eliminate disturbances
High pressure required

## Slide 6
ASSUMPTION DATA FROM PAPERS AND CADs
World frame position: left edge of the wing
Flap revolute joint position: (0.365, 0.145) [m]
Flap measures: 1.01 x 0.152 x 0.02 [m]
Flap material : carbon fiber (density = 2100 [kg/])
Piston diameter : 0.02 [m]
Piston material : steel (density = 7500 [kg/])

## Slide 7
ASSUMPTION EXTERNAL AERODYNAMIC TORQUE

## Slide 8
ASSUMPTION PROFILE OF THE ANGLE OF THE FLAP

## Slide 9
ASSUMPTION PROFILE OF THE ANGLE OF THE FLAP

## Slide 10
PUSH UP Mechanism Description

## Slide 11
PUSH UP Position analysis
Constraint equation
Range of motion of the piston Initial configuration problem
Position analysis

## Slide 12
PUSH UP Motion of the mechanism
Angle of the flap: 35°
Piston displacement: 8 cm
Length of the rod: 13 cm

## Slide 13
PUSH UP Velocity analysis
Velocity ratio
Singular configurations

## Slide 14
PUSH UP Principle of virtual work
Virtual displacements of the center of mass of the piston and the flap and the rotation of the flap
External forces that acts on the mechanism
Static conditions

## Slide 15
PUSH UP Newton Euler approach
Reaction forces:
  Prismatic joint: force and torque (Rbx(t), Tb(t));
  Rod joint between the flap and the piston: tension, since it is assumed massless, (Rr(t));
  Revolute joint between the flap and the ground (Rex(t), Rey(t));

## Slide 16
PUSH UP Lagrange approach
Used in order to have less equations in the dynamic optimization part
It involves directly the constraint equation (associated to the rod joint) using λ1(t)

## Slide 17
PUSH UP ODE resolution
Imposing a given trajectory to the flap, it’s possible to solve an ODE imposing the initial conditions for the reaction forces (case of Newton – Euler approach) and lambda (case of Lagrange approach), for the initial position and velocity of the piston and for the initial value of the piston force.

## Slide 18
PUSH UP INVERSE DYNAMIC resolution
INVERSE DYNAMIC resolution
Initial conditions
Inverse kinematic analysis in order to obtain the trajectory of the piston
Algebraic problem used to find the reaction forces (or lambda1) and the force of the piston Fp
Piston Force Fp(t)
Maximum value: 940.000005224270N

## Slide 19
PUSH UP DAE resolution
Dae Resolution
Index reduction step by step using a LUDecomposition
Index reduction using Bertolazzi’s toolbox
Initial conditions for positions and velocities of the flap and the piston and for the reaction forces
DAE resolution using dsolve and imposing a given force to the piston

## Slide 20
POD ROCKER-KINEMATIC ANALYSIS

## Slide 21: POD ROCKER-KINEMATIC ANALYSIS POSITION ANALYSIS – DIRECT KINEMATIC (qI = xP)

## Slide 22: POD ROCKER-KINEMATIC ANALYSIS POSITION ANALYSIS – DIRECT KINEMATIC (qI = xP)

## Slide 23: POD ROCKER-KINEMATIC ANALYSIS POSITION ANALYSIS – DIRECT KINEMATIC (qI = thetaW)

## Slide 24: POD ROCKER-KINEMATIC ANALYSIS POSITION ANALYSIS – DIRECT KINEMATIC (qI = thetaW)

## Slide 25: POD ROCKER-KINEMATIC ANALYSIS POSITION ANALYSIS – DIRECT KINEMATIC (qI = thetaW)

## Slide 26: POD ROCKER-KINEMATIC ANALYSIS VELOCITY ANALYSIS – VELOCITY RATIOS

## Slide 27: POD ROCKER-KINEMATIC ANALYSIS VELOCITY ANALYSIS – SINGULAR CONFIGURATIONS
xP(t)=0.1993212061, thetaT(t)=0.1058421609, thetaW(t)=0.4325729110
xP(t) = 0.1204449791,
thetaT(t) = 1.692504172, thetaW(t) = -0.001786259444

## Slide 28
POD ROCKER-DYNAMIC ANALYSIS

## Slide 29: POD ROCKER-DYNAMIC ANALYSIS PVW – PISTON FORCE IN STATIC CONDITIONS
MaxFp = 330.61642472216977 @ xP = 0.14283656557531654

## Slide 30: POD ROCKER-DYNAMIC ANALYSIS NE – INVERSE DYNAMIC

## Slide 31: POD ROCKER-DYNAMIC ANALYSIS NE – INVERSE DYNAMIC
Max piston force: 943.0621997

## Slide 32: POD ROCKER-DYNAMIC ANALYSIS LG – DIRECT DYNAMIC
Initial conditions:

## Slide 33
POD – PULL MECHANISM
KINEMATIC ANALYSIS

## Slide 34
POD – PULL MECHANISM
POSITION ANALYSIS – DIRECT KINEMATIC

## Slide 35
POD – PULL MECHANISM
POSITION ANALYSIS – DIRECT KINEMATIC

## Slide 36
POD – PULL MECHANISM
POSITION ANALYSIS – INVERSE KINEMATIC

## Slide 37
POD – PULL MECHANISM
ANIMATION

## Slide 38
POD – PULL MECHANISM
VELOCITY RATIOS – INVERSE KINEMATIC

## Slide 39
POD – PULL MECHANISM
KINEMATIC ANALYSIS

## Slide 40
POD – PULL MECHANISM
DYNAMIC ANALYSIS

## Slide 41
POD – PULL MECHANISM
DYANAMICS - PRINCIPLE OF VIRTUAL WORK

## Slide 42
POD – PULL MECHANISM
DYANAMICS - PRINCIPLE OF VIRTUAL WORK

## Slide 43
POD – PULL MECHANISM
NEWTON – EULER APPROACH

## Slide 44
POD – PULL MECHANISM
LAGRANGE APPROACH

## Slide 45
POD – PULL MECHANISM
ODE RESOLUTION – INITIAL CONDITIONS

## Slide 46
POD – PULL MECHANISM
INVERSE DYNAMICS RESOLUTION

## Slide 47
POD – PULL MECHANISM
REACTION FORCES

## Slide 48: HYDRAULICS

## Slide 49
HYDRAULICS PUSH-UP MECHANISM

## Slide 50
HYDRAULICS POD-ROCKER MECHANISM
max pressure: 29.92994460

## Slide 51
HYDRAULICS POD-PULL MECHANISM

## Slide 52
COMPARISON
SPECS | PUSH - UP | POD - ROCKER | POD - PULL
Piston displacement [m] | 0.0802 | 0.0438 | 0.0646
Avg velocity ratio [-] | -7.909 | -13.65 | 6.286
Max force [N] | 940.0 | 943.1 | 1287.9
Max power [W] | 1120 | 1176 | 1224
# of bodies | 2 | 3 | 2
# of joints | 3 | 5 | 3
Max tot reaction force [N] | 3366.98 | 5883.80 | 3475.61
Extra weight [kg] | - | + 0.0119 | -